## Slide 1: Low Carbon refurbishment of Heritage Buildings
Andy Sheppard
Arup

## Slide 2: The project & team
Carbon reductions in Listed Buildings
  Generic guidance document
  Five case studies
Notes: This project was all about the potential of the case study buildings to be transformed into lower carbon buildings. Will also throw in some examples of where it’s been carried out to show it is really possible.

## Slide 3: Heritage Assets context
Buildings: 40% of UK carbon emissions
Whole sector zero carbon by 2050
80% of buildings already built
  374,081 listed building (92% Grade II)
  9,080 conservation areas
Notes: A bit of context –
40% of UK’s emissions come from buildings
Sector as a whole needs to be zero carbon by 2050
Nearly 400,000 Listed Buildings, 9000 conservation areas

## Slide 4: Guidance: Overview
The intended audience:
  Planning and conservation officers
  Architects
  Building owners
The aim:
  To demystify the process and the options

## Slide 5: Guidance: Investigate
Bill analysis – basic but essential
Benchmarking can be challenging
Sub-metering very useful
Range of supplementary tests possible
  Thermal imaging
  Air pressurisation
  In-situ U-value
  Thermal modelling
Notes: Benchmarking – make sure you’re comparing like-with-like and that internal conditions are satisfactory
Supplementary tests include many options. Which is carried out will depend on the which areas would seem to benefit from additional investigation.

## Slide 6: Study: Manchester Art Gallery
Lighting 50% of electrical consumption
Upgrade
  LEDs
  Occupancy sensors, programmable controls
Energy reduced by 89%
Next phase targeting a further 40%

## Slide 7: Guidance: Intervention
Think about the building as a whole
Energy hierarchy
  Apply with pragmatism
Behaviour – has to be first
Fabric – possible with care
Services – more freedom
Low carbon – perfectly feasible
As necessary | Recommissioning
Minor refurbishment | Controls
Major refurbishment | Plant replacement, metering
Notes:   Holistically - There can be unexpected consequences of action:
Historic buildings need to breathe
  Condensation and moisture control is important
Fabric interventions may not be feasible
Fabric – from air-tightness to insulation. Not all of most buildings are important in terms of heritage. Pick your areas carefully
Services – improvements can be incorporated into refurbishment cycles often with little on-cost over the standard like-for-like replacement

## Slide 8: Study: Scotstoun House
Notes: Edinburgh - Grade B listed, 1960’s. Refurbishment and extension.
Refurbishment took the 24m deep building to a natural ventilation strategy. Also biomass boiler, light-tubes, phase change thermal mass, roof passive ventilators
30% reduction in heating energy
60% reduction in lighting energy

## Slide 9: Study: 39 Hunter St, Sydney
Notes: Constructed 1916. Permanent conservation order by NSW Heritage Council
Heavily shaded by surrounding buildings
Refurbishment greatly improved daylighting, particularly through the use of a new atrium
Removal of ceilings to expose thermal mass
Highest GreenStar Rating, 5 star energy rating. Quickly leased to Blue-chip company for 15 year term

## Slide 10: Case Studies
Heritage value & Statement of Significance
Building condition survey
Bill analysis & benchmarking
Interventions listing
Options Appraisal
Recommendations
Notes: Heritage survey showed varying importance across the building
Condition survey invariably showed up aspects of fabric and systems that were in need of replacement so upgrades could be incorporated at a lowered on-cost

## Slide 11: Mercer Gallery
Heritage importance within
  Windows, doors and interiors
Controls, monitoring, behaviour
Larger scale interventions
  Hot water system
  Roof insulation (+ wall?)
  LED lighting
  Photovoltaics?
20%
40%
60%
80%
100%
!
Elec
Gas
<5
<10
>10
Notes: Care over summation of intervention results

## Slide 12: St. Peters Street
Heritage importance within
  Some windows, panelled reveals, roof spaces
Unsure future use
Larger scale interventions
  Loft insulation (with care)
  Lighting controls
  Draught stripping
  Internal wall insulation feasible
  High performance secondary glazing
20%
40%
60%
80%
100%
Elec
Gas

## Slide 13: Armley Mills
Heritage importance within
  Pretty much everything!
Monitoring, controls
Larger interventions
  Boiler modernisation
  Digital plant controls
  Partial roof insulation
  Daylight linking in lights
20%
40%
60%
80%
100%
Elec
Gas

## Slide 14: Almondbury Dwelling
Heritage importance within
  Exterior walls and roof, some interior
Recently upgraded
Larger interventions
  Tailor to occupant
  Draught-stripping
  Low energy lighting
  Loft insulation
  Wall, floor insulation feasible
20%
40%
60%
80%
100%
Elec
Gas
Notes: Recent upgrades meant energy bills were unrelated to the current state of the building
Payback period of heating load reductions raises an interesting question. Should we discount paybacks at this period when the building has been around for 130 years and may well see the same again?

## Slide 15: Lord Deramore’s School
Heritage importance within
  Exterior, some interior
Emissions 86% heating
Larger scale interventions
  Roof and wall insulation possible
  Boiler system & controls
  Secondary glazing
  Photovoltaics
20%
40%
60%
80%
100%
Elec
Gas

## Slide 16: Fabric possibilities
Chart: Percentage gas / oil savings
| Mercer Gallery | St Peters Street | Armley Mills | Lord Deramore's | Mercer Gallery | St Peters Street | Weaver's Cottage | Lord Deramore's
Series 1 | 0.075 | 0.12 | 0.04 | 0.075 | 0.15 | 0.2 | 0.35 | 0.2
Roof
Walls
  Maintain ventilation pathways
  Be aware of bats
  Heritage impact often ‘manageable’
    But take care!
  Longer payback
    >10 years

## Slide 17: Glazing possibilities
Chart: Percentage gas / oil savings
| Mercer Gallery | St Peters Street | Armley Mills | Weaver's Cottage | Lord Deramore's | St Peters Street | Armley Mills | Weaver's Cottage | Lord Deramore's
Series 1 | 0.04 | 0.04 | 0.07 | 0.06 | 0.04 | 0.1 | 0.05 | 0.2 | 0.1
Draught-proofing
Secondary gl.
  Good English Heritage research
  Already in some areas
    >10 year payback

## Slide 18
Take away that:
  The heritage process is no more difficult
  Starting with the basics can yield good results
  With care, larger interventions can be identified
  Significant savings are possible

## Slide 19
Thanks
andy.sheppard@arup.com
www.yourclimate.org/pages/low-carbon-heritage-buildings